## Slide 1: Capstone project proposal: EM parameterization of CF composite
Sponsor: Tangitek LLC
Advisor: Branjmir Pejcinovic
Students: Ha Tran, Thanh Le, Jeffrey Brown

## Slide 2: Requirements From Project Description
From 300 MHz to 30 GHz
EM parameter extraction:
  Dielectric constant
  Complex electric permittivity
  Complex magnetic permeability
  Loss tangent
  Layer thickness
Simulation model for validation
NRL arch measurement

## Slide 3: Project Management
Trello, GitHub, Gantt Chart
Project main phases:
  Project Initialization: Research for approaches of material characterization
  Prototype: NRL arch and waveguide with current part availability. Absorption coeffect of control sample (PVC) is calculated and compared with previous result
  Optimization: Cover all frequency ranges, arch for antenna, antenna chamber.
  Presentation: PSU capstone presentation

## Slide 4: Technical Approach: NRL Arch and Waveguide
NRL Arch
  Advantage: Industrial standards, different incident/reflection angles
  Disadvantage: Big sample size (greater than 5 lambda), antenna alignment
Waveguide
  Advantage: Higher dynamic range, small sample size
  Disadvantage: sample preparation (require perfect contact between sample and waveguides)

## Slide 5: NRL Arch Prototype: Measurement Setup
VNA is used as both the stimulus and detector of microwave signals
Signal from the reflective plate (without the sample) provides a reference signal for calibration
Reflectivity in dB = 10*log10 (P1/P0)
Absorption coefficient of PVC is calculated and compared.
An arch with positioners will be built to measure reflection for different incident angles

## Slide 6: Waveguide Prototype: Measurement Setup
L: a segment of rectangular waveguide where a sample has been placed
L1, L2: hollow rectangular waveguide
Port 1 and Port 2 are connected to VNA
using adapters.
Equations for complex epsilon and mu are provided in Microwave Electronics: Measurement and Materials Characterization
L.F. Chen et al 2004,
Microwave Electronics: Measurement and
Materials Characterization

## Slide 7: Procedures: Optimization
Interactive Solver: Solving both material thickness and material properties at the same time. Provide higher accuracy.
NRL Arch measurement in RF chamber
Partially filled waveguide
EM simulation: EM Pro, avaialble for students at PSU
Modeling

## Slide 8: Available Parts: Antennas
SAS-510-4 Log Periodic Antennas
Frequency Range: 290 MHz to 4 GHz
Physical dimension: 60.4 cm x 51.1 cm
Adjustable Dipole (400 MHz to 1 GHz), and horn antenna in X-band is also avaialble at PSU

## Slide 9: Available parts: Waveguides
PSU has waveguide and adapter in X-band (figure)
We still need to find a sample holder (a segment of X-band waveguide that has suitable size for the sample) and a TRL calibration kits
  Reflect standards: A X-band waveguide short termination
  Line standards: A X-band waveguide segment (90 degree long line at center frequency)

## Slide 10: Potential Problems and Needs
Potential problems:
  Required sample size for NRL arch measurement in low frequency will be too large.
  Surrounding environment may affect the measurement for both setups
  Sample preparation for waveguide measurement is not perfect and hard to detect.
Needs:
  Sample with various sizes for different frequency range
  Antennas for frequency range 4 – 8 Ghz and above 12 Ghz
  Waveguide sample holders
  Waveguide for other frequency range (except X-band)

## Slide 11: Current Status
Finish detail time plan (using Gantt chart).
Finish researching and literature review.
Finish gathering parts avaialble at PSU. We need detailed information about sample size and antenna/waveguide printing capability.
Equations and measurement setup for prototype of NRL arch and waveguide are available.

## Slide 12: Related Documents and References
All related documents are available on GitHub https://github.com/trankhiemha/ECE412-413-Capstone-Project-N3
Project progression tracking is available on Trello https://trello.com/b/Ov0bqGiB/initial-cf-planning
Research papers are on Zotero page: https://www.zotero.org/groups/957151/items