## Slide 1: Capstone project proposal presentation: EM parameterization of CF
Students: Ha Tran, Thanh Le, Jeffrey Brown
Advisor: Branjmir Pejcinovic
Sponsor: Tangitek LLC

## Slide 2: Requirements from project description
From 300 MHz to 30 GHz
Dielectric constant, complex electric permittivity, magnetic permeability, loss tangent and layer thickness
Simulation model for validation
NRL arch

## Slide 3: Project management
Trello, GitHub, Giant Chart
Project main phase
  Project Initialization: Research for approaches of material characterization
  Prototype: NRL arch and waveguide with current part availability. Absorption coeffect of control sample (PVC) is calculated and compared with previous result
  Optimization: cover all frequency ranges, arch for antenna, antenna chamber.
  Presentation: PSU capstone presentation

## Slide 4: Technical approach: NRL Arch and waveguide
NRL Arch
  Advantage: Industrial standards, different incident/reflection angles
  Disadvantage: Big sample size (greater than 5 lambda), antenna alignment
Waveguide
  Advantage: Higher dynamic range, small sample
  Disadvantage: sample preparation (require perfect contact between sample and waveguides)

## Slide 5: NRL arch prototype: Antennas
-for more info…List location or contact for specification (or other related documents)
SAS-510-4 Log Periodic Antennas
Frequency Range: 290 MHz to 4 GHz
Physical dimension: 60.4 cm x 51.1 cm
Adjustable Dipole (400 MHz to 1 GHz),
and horn antenna in X-band is also avaialble at PSU

## Slide 6: NRL arch prototype: Measurement setup
VNA is used as both the stimulus and detector of microwave signals
Signal from the reflective plate (without the sample) provides a reference signal for calibration
Reflectivity in dB = 10*log10 (P1/P0)
Absorption coefficient of PVC is calculated and compared.

## Slide 7: Waveguide prototype: measurement setup
L: a segment of rectangular waveguide where a sample has been placed
L1, L2: hollow rectangular waveguide
Port 1 and Port 2 are connected to VNA
using adapters.
Equations for complex epsilon and mu are provided in Microwave Electronics: Measurement and Materials Characterization
L.F. Chen et al 2004,
Microwave Electronics: Measurement and
Materials Characterization

## Slide 8: Waveguide prototype: parts
PSU has waveguide and adapter in X-band (figure)
We still need to find a sample holder (a segment of X-band waveguide that has suitable size for the sample) and a TRL calibration kits
  Reflect standards: A X-band waveguide short termination
  Line standards: A X-band waveguide segment (90 degree long line at center frequency)

## Slide 9: Procedures: optimization
-for more info…List location or contact for specification (or other related documents)
Interactive Solver: Solving both material thickness and material properties at the same time. Provide higher accuracy
Arch for antenna:
Partially filled waveguide:
EM simulation: EM Pro, avaialble for students at PSU
Modeling:

## Slide 10: Current Status
Finish gathering parts avaialble at PSU. We need detailed information about sample size and antenna/waveguide printing capability
Equations and measurement setup for prototype of NRL arch and waveguide are avaialble.

## Slide 11: Related Documents and References
GitHub: https://github.com/trankhiemha/ECE412-413-Capstone-Project-N3
Trello page: https://trello.com/b/Ov0bqGiB/initial-cf-planning
All related documents are available in GitHub
Project progression tracking is available in Trello